## Slide 1: FPGA原型验证
2024年10月11日

## Slide 2: 实验6：FPGA原型验证
从lab2\vivado\rvfpganexys.tcl文件恢复Vivado工程
打开Vivado界面
Window -> Tcl Console
cd lab2\vivado
  切换到rvfpganexys.tcl文件所在目录
source rvfpganexys.tcl
  在lab2\vivado目录下生成工程目录rvfpganexys及工程文件rvfpganexys.xpr
执行脚本，添加include路径（source rvfpganexys.tcl没有正确执行）
  set_property -name "include_dirs" -value "[file normalize "$origin_dir/../src/VeeRwolf/Interconnect/AxiInterconnect/pulp-platform.org__axi_0.25.0/include"] [file normalize "$origin_dir/../src/VeeRwolf/VeeR_EL2CoreComplex/include"] [file normalize "$origin_dir/../src/OtherSources/pulp-platform.org__common_cells_1.20.0/include"]" -objects $obj
Generate Bitstream生成位流
查看Synthesis和Implementation阶段的报告

## Slide 3: 生成位流-Bitstream Generation
为当前项目选择的目标FPGA器件生成位流，基于项目的流程：
  IDE方式: Flow Navigator -> Program and Debug -> Generate bitstream
  Tcl脚本方式: launch_runs impl_1 -to_step write_bitstream
位流文件格式
  -raw_bitfile: 生成ASCII格式的原始位流文件 (.rbt)
  -bin_file: 生成二进制位流文件 (.bin)，只包含器件编程数据，没有头部信息，可以用来烧写FLASH
  -logic_location_file: 生成包含LUT、BRAM、FF、IOB的位置信息的文件(.ll)
  缺省生成.bit文件

## Slide 4: Synthesis Report
Synthesis
  ->Open Synthesized Design
    -> Report Utilization

## Slide 5: Synthesis Report
Synthesis
  ->Open Synthesized Design
    -> Report Timing Summary

## Slide 6: Implementation Reports
Implementation
  ->Open Implementation Design
    -> Report Utilization

## Slide 7: Timing Report
Implementation
  ->Open Implementation Design
    -> Report Timing Summary